11.4 SINGLE-STAGE MODULE CALCULATIONS: These equations mathematically describe the performance of a single-stage thermoelectric module as illustrated in Figure (11-l). When entering numerical data, do not forget that temperature values must be expressed in degrees Kelvin (°K). Calculations of the various parameters should be performed in the order shown.

Figure (11-1)
a) The temperature difference (DT) across the module in °K or °C is:
DT = Th – Tc
b) Heat pumped (Qc) by the module in watts is:
Qc = (SM × Tc × I) – (0.5 × I2 × RM) – (KM × DT)
c) The input voltage (Vin) to the module in volts is:
Vin = (SM × DT) + (I × RM)
d) The electrical input power (Pin) to the module in watts is:
Pin = Vin × I
e) The heat rejected by the module (Qh) in watts is:
Qh = Pin + Qc
f) The coefficient of performance (COP) as a refrigerator is:
COP = Qc / Pin
Extract peltier parameters from performance Curve (Qc vs DeltaT)

We can solve eq. (b) for K

K= {S*T_c*I-0.5*I^2*R-Q_c} over {DT}

we can choose two points 1 and 2 on the Curve where Qc = 0 so we have

{S*T_c1*I_1-0.5*I_1^2*R} over {DT_1} = {S*T_c2*I_2-0.5*I_2^2*R} over {DT_2}

S* left ({T_c1*I_1} over {DT_1} - {T_c2*I_2} over {DT_2} right) = 0.5*R* left ({I_1^2} over {DT_1} - {I_2^2} over {DT_2} right)

S* (T_c1*I_1*DT_2 - T_c2*I_2*DT_1) = 0.5*R* (I_1^2*DT_2 - I_2^2*DT_1)
R =S*2* left ( {T_c1*I_1*DT_2 - T_c2*I_2*DT_1} over {I_1^2*DT_2 - I_2^2*DT_1} right ) = S*A

if whe consider point 3 in the performance Curve where dT=0 we can write

Q_c= S*T_h*I_1-0.5*I_1^2*R = S*(T_h*I_1-0.5*I_1^2*A )

S= {Q_c} over {T_h*I_1-0.5*I_1^2*A }

R= S*A

finally we can consider again point 3 where Qc = 0 in order to calculate K

K= {S*T_c1*I_1-0.5*I_1^2*R} over {DT_1}